## Slide 1: Exercise: CHERI Pointer Integrity Introduction
Spatial safety depends upon reference/pointer integrity
  Pointers must come from other pointers.
  Can’t forge a reference (and associated bounds) arbitrarily
CHERI tags prevent confusion between data per se and capabilities
📖Demonstrate CHERI Tag Protection 👩‍💻!

## Slide 2: Exercise: CHERI Pointer Integrity Discussion: Contrasting Baseline and CHERI
Exercise program constructed “the same” pointer two different ways:
  By setting the last byte of a pointer in memory
  By transforming the address of a language-level pointer
RISC-V Baseline
q=0x80ec2000 (0xb7 into buf)
*q=b7
r=0x80ec2000 (0xb7)
*r=b7
CHERI-RISC-V
q=0x3fffdffe00 [rwRW,0x3fffdffd71-0x3fffdfff70] (0x8f into buf)
*q=8f
r=0x3fffdffe00 [rwRW,0x3fffdffd71-0x3fffdfff70] (invalid) (0x8f)
In-address space security exception

## Slide 3: Exercise: CHERI Pointer Integrity Discussion: gdb
Program received signal SIGPROT, CHERI protection violation
Capability tag fault caused by register cs1.
main () at ./src/exercises/cheri-tags/corrupt-pointer.c:45
Thread 1 (LWP 100057 of process 1231):
#0 main () at ./src/exercises/cheri-tags/corrupt-pointer.c:45
(gdb) p $_siginfo
$1 = {si_signo = 34, si_errno = 0, si_code = 2, … _reason = {_fault = {si_trapno = 28, si_capreg = 9}, …
AKA PROT_CHERI_TAG

## Slide 4: Exercise: CHERI Pointer Integrity Discussion: Investigating the Opcodes
CHERI data instructions clear tags, capability instructions preserve
  Tagged capabilities have provenance that is exclusively capability instructions
  Initial tagged quantities provided in registers at boot!
Ptr | Op | Baseline | CHERI
r | Store | sb zero, 0(sp) | csb zero, 32(csp)
 | Load | ld s0, 0(sp) | clc cs1, 32(csp)
q | Load | ld a0, 0(sp) | clc ca0, 32(csp)
 | Extract |  | cgetaddr a1, ca0
 | Mask | andi s0, a0, -256 | andi a1, a1, -256
 | Update |  | csetaddr cs1, ca0, a1
📚 CHERI Instruction-Set Architecture (Version 8)